## Slide 1
Overview/Topics
Terminology
  Corrosion/Rust
  Cathodic protection
  Sacrificial anodes
  Electrolysis
Skills to Master
HW 16e
Read
OER 16.6-16.7
CHE 112 Spring 2021
Lecture 16e – Corrosion and Electrolysis

## Slide 2
Corrosion
Degradation of metals by a naturally occurring electrochemical process
Rust, Tarnish, Patina etc.
Costs $500 billion a year!
20% of Fe production used to replace rusted parts
The more reactive a metal the faster it corrodes. Ex: Na
Normally forms an oxide layer
Fe
Ag
Cu

## Slide 3
Rust - Fe
Anode loses mass
Cathode gains mass
Combination of reactions
No protective layer formed
Speeds up if:
  Aqueous (wet)
  acidic solution
  salts NaCl etc
  Temperature

## Slide 4
Corrosion Prevention
Protective Layers
Formation of alloys
Galvanization
Cathodic Protection
Sacrificial Anodes
Protective Layers
Prevent contact between metal and O2
Paint, Oil, Plastic, Grease, Tin (Sn cans)
Electroplating Cr (Chrome plating)
https://sciencing.com/tin-cans-made-5344942.html
https://oceanfootprint.co.uk/rust-prevention-101-nyalic-the-guide/

## Slide 5
Galvanization
Layer of more readily oxidized metal
Oxidizes first, forms protective layer
Ex: Zn reacts to form ZnO or Al forms Al2O3
Two types of protection
Oxidized first, Protective Layer

## Slide 6
Cathodic Protection
Cathodic protection (CP) is a technique used to control the corrosion of a metal surface by making it the cathodic side of an electrochemical cell. The simplest method to apply CP is by connecting the metal to be protected with another more easily corroded metal to act as the anode of the electrochemical cell
Sacrificial Anode
Connect Iron to a more reactive metal to supply e- instead of Fe
Commonly Zn – ships (right) or Mg – pipe (book)
“Sacrificial” because used up.
Cheaper to replace sacrificial anode than iron in ships/pipes

## Slide 7
Fe (s) → Fe+2 (aq) + 2 e-
Anode:
http://www.dynamicscience.com.au/tester/solutions1/chemistry/corrosion/rustpreventionsacanode.htm
Replace Fe with more active metal
i.e. easier to oxidize
(lower on chart)
Zn (s) → Zn+2 (aq) + 2 e-
Mg (s) → Mg+2 (aq) + 2 e-
Example
Zn or Mg is the new anode, therefore Fe would act as an cathode and not lose electrons

## Slide 8
Connect to battery or other source to supply e- instead of the Fe
Cathodic Protection
https://www.metallurgyfordummies.com/how-cathodic-protection-works.html

## Slide 10
Alloys
Alloy Fe with other metals that oxidize easier to form protective layers
Stainless steel
Chrome plating Cr2O3 (s)
Expensive
https://www.engineeringclicks.com/chrome-plating/

## Slide 11
Ag
https://www.instructables.com/Polishing-Silver-Two-Fast-Effortless-Methods/
Try it:
Which E is oxidized?
Which E is reduced?

## Slide 12
Write the chemical reactions for Ag and Al.
Label the Anode and Cathode.
Calculate
Spontaneous or Nonspontaneous?
Try it:

## Slide 13
Real Life is a bit more complicated…

## Slide 14
Electrolysis
Reverse of a galvanic cell
External source of e- to drive a redox reaction in the reverse (nonspontaneous) direction
Many important uses
  Recharge batteries
  Separation and Purification of metals
  Production of many chemical
  Electroplating of metals
“electrolytic cells”
Examples from Book:
Molten NaCl to produce Na (s) + Cl2 (g)
Water to produce H2 and O2 gas
Aqueous NaCl to produce NaOH and Cl2 (g)
Electroplating Ag

## Slide 15
What does 0 tell us?

## Slide 16
Applications of Electrolysis
Examples from Book (read them)
  Water to produce H2 and O2
  NaCl (s) to produce Na (s), Cl2
  NaCl (aq) to produce H2 , Cl2 + 2 OH-
$4 billion/year industry
13 million tons Cl2
10 million tons NaOH
https://chemed.chem.purdue.edu/genchem/topicreview/bp/ch20/faraday.php#:~:text=The%20deciding%20factor%20is%20a,water%20to%20O2%20gas.
Molten NaCl (l)

## Slide 17
Analyzing Electrolytic Cells
Identify all possible reactions (including water if (aq))
Determine reaction most likely to be reduced)
Determine reaction most likely to be oxidized)
Write and balance ½ reactions
Determine
Sketch picture of cell (ie HW 16b)
Strongest OA = + value closest to zero
Strongest RA = - value closest to zero
< 0 (non-spont)
“Reverse of a battery”
Overvoltage
= minimum amount of energy to reverse a reaction in “ideal” conditions
Extra voltage that must be applied to a reaction to get it to occur at the rate at which it would occur in an ideal system
Often quite substantial
Complicated – hard to calculate
Ignore it in calculations!

## Slide 18
Molten NaCl (l)
Aqueous NaCl (aq)
Reactions that can occur
Choose reactions/write ½ reactions
Reactions that can occur
Choose reactions/write ½ reactions
= -2.71 V
= +1.23 V
= +1.36 V
= +1.36 V
= 1.36 V
HW/Test Question – what is the difference in the Electrolytic Cells between NaCl (s) and NaCl (aq)?

## Slide 19
Aqueous NaCl (aq)

## Slide 20
Try It:
In electrolytic cell composed of aqueous KI:
List possible reactions
Determine most likely to be oxidized (smallest +)
Determine most likely to be reduced (smallest -)
Write ½ cell reactions
Calculate

## Slide 22
Try It:
List possible reactions
Determine most likely to be oxidized
Determine most likely to be reduced
Sketch the Cell
Write ½ cell reactions
Calculate

## Slide 24
Electroplating
Metal A more reactive than Metal B
Metal A is lower on the chart
Solution: Salt of metal B
e-
e-
e-
C+
Opposites attract
B (s) → B+ (aq) + e-
B+ (aq) + e- → B (s) + e-

## Slide 25
Try It
Sketch an electrolytic cell for a Ni electrode and an Fe electrode
Label Cathode, Anode, +/-, battery, direction of e- flow, solution, gain/loss of mass
Write the possible reactions occurring at the anode
Write the possible reactions occurring at the cathode
Write the ½ reactions and net reaction that will occur.

## Slide 27
Electrorefining
Similar to Electroplating but used to purify metals
e-
Cu+
Impure
Pure
https://www.ausetute.com.au/electrorefine.html#:~:text=Electrorefining%20Copper&text=The%20electrolyte%20containing%20the%20copper,push%20them%20to%20the%20cathode.

## Slide 28
Label Anode and Cathode
Write the ½ reactions for Zn, Fe, Ni, Ag, Au, Cu.
Which ½ reactions occur at the anode?
Which ½ reactions occur at the cathode?
Which ½ reactions won’t occur?
Calculate
Try It

## Slide 29
Electrolysis Math
Current = Rate of e- flow (a)
Time = how long it flows (varies)
Current x Time
Amount of Charge
F = Faraday Constant
charge on 1 mole of e-
96,500 C/mol e-
96,500 J/V·mol
Moles e-
Moles
R or P
g/L etc
R or P
mol/mol ratio
MW or M

## Slide 30
Production of Al
Hall-Heroult Process (1866)
  Hall = 22
  Heroult = 23
Low voltage (5-6 V)
High Current (250,000 A)
1 mol e- makes 9 g Al
5% of energy production in US
Recycling costs 1/70th amount
https://www.aluminum.org/industries/production/primary-production
Al (mp) = 2045 °C
Cryolyte = 800-1000 °C

## Slide 31
Example:
How many grams of Al are produced in 1 hour by the electrolysis of AlCl3 if the applied current is 10 A?

## Slide 32
Example:
Calculate the number of kilowatt-hours (kW·hr) required to produce 1000. kg of Al at an applied EMF of 4.50 V.

## Slide 33
Example:

## Slide 34
Example:

## Slide 39
Patina - Cu
Forms long lasting coating that is water resistant (useful property) Often desirable because “pretty”
Artificial methods for patina formation
In the reaction below:
What is oxidized?
What is reduced?
Try It
https://en.wikipedia.org/wiki/Patina

## Slide 40
Complex Process
Involves lots of chemical reactions
Time/Temperature variables
Too much work for us!
https://copperalliance.org.uk/knowledge-base/education/education-resources/copper-reactivity-patination/

## Slide 41
https://www.sciencecompany.com/Patina-Formulas-for-Brass-Bronze-and-Copper.aspx
Artificial Patina’s